## Slide 1
SUMMER DEMO
PARKING FINDER
The most efficient problem for tackling modern problems is using modern solutions.
ATU FINAL YEAR PROJECT
SEAN MALONEY
GITHUB

## Slide 2
THE PROJECT OVERVIEW
  Smart parking prototype using AI and computer vision
  Detects vehicles and classifies spaces as free or occupied
  Built with YOLOv8, Raspberry Pi, FastAPI, MongoDB, and Next.js
  Includes parking visualisation and A* route generation
  Designed as a low-cost parking assistance solution
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 02

## Slide 3
FINAL ARCHITECTURE
DIAGRAM
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 03
A Next.js frontend on a Raspberry Pi LCD touchscreen displays parking status, detections, and route results to the user.
USER INTERACTION & OUTPUT
FastAPI manages the core logic, connecting MongoDB storage, YOLOv8 vehicle detection, and C++ A* pathfinding.
BACKEND, AI & ROUTING
03
04
02
A Raspberry Pi camera captures parking images, and the Raspberry Pi 4 uploads them to the backend over Wi-Fi.
IMAGE CAPTURE & UPLOAD
Parking Finder is a smart parking system that integrates image capture, AI detection, parking analysis, and route generation.
SYSTEM OVERVIEW
01
02
03
04

## Slide 4
WHAT’S NEW SINCE CHRISTMAS DEMO?
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 04
Redesigned the frontend with an Ookla Speedtest inspired layout and improved overall system integration across hardware, backend, AI, and routing.
FRONTEND & SYSTEM IMPROVEMENTS
Added parking polygon configuration, occupancy classification, and C++ A* pathfinding to generate routes to available spaces.
PARKING ANALYSIS & ROUTING
Integrated MongoDB for persistent storage of parking configurations, metadata, and capture data.
DATABASE & STORAGE
Added Raspberry Pi camera capture, Raspberry Pi 4 upload flow, and LCD touchscreen support.
PI INTEGRATION
03
04
02
01
02
03
04

## Slide 5
CHALLANGES AND SOLLUTIONS
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 05
Challenge: Training was initially on CPU instead of GPU due to CUDA, PyTorch, and driver version mismatches.
Solution: Researched CUDA compatibility matrices, aligned software versions to successfully enable GPU.
GPU TRAINING & CUDA COMPATIBILITY
Challenge: The original drone based idea was not practical for a realistic parking deployment.
Solution: Redesigned around a fixed elevated camera for a more practical and reliable solution.
CAMERA APPROACH & SYSTEM DIRECTRION
Challenge: Vehicle detection alone could not identify free spaces.
Solution: Parking polygons were added for space classification.
OCCUPANCY CLASSIFICATION
Challenge: Route generation depended on accurate grid mapping.
Solution: A C++ A* system was integrated for routing.
PATHFINDING & GRID SETUP
01
02
03
04

## Slide 6
RESEARCH
  Parking space configuration
  Occupied vs free space detection
  A* route generation
  Grid layout mapping
  MongoDB data storage
  Raspberry Pi integration
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 06

## Slide 7
PROJECT MANAGEMENT 1
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 07
SEMESTER 2
SEMESTER 1
VS

## Slide 8
PROJECT MANAGEMENT 2
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 08
  Sprint based development
  Clear improvement from Semester 1→ Semester 2
  Better task breakdown and estimation over time
  Moved to 2/1 week sprints for easier management
  Gannt chart used for easier planning.
  Jira used to track sprint progress and priorities
  GitHub network reflects improving and structured workflow
  OneNote used to document project progress

## Slide 9
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 09
YOLO AND A*
C++ A* Algorithm Pathfinder
YOLOv8 Vehicle Detection
A* is a pathfinding algorithm used to find the shortest or most efficient path between two points.
It works by comparing the cost already travelled with an estimate of the cost remaining to the goal.
YOLOv8 is an object detection model used to identify and locate objects within an image.
It works by predicting bounding boxes and class labels in a single pass, making it fast and effective for real time detection.
01
02

## Slide 10
·Generative AI tools were used as support tools during the preparation of this project.
·AI assistance, where used, was used for tasks such as brainstorming, language refinement, formatting support, structure planning, debugging, generation of code, rewriting of code, and web scraping information not easily found.
·All technical design, implementation, testing, evaluation, and final written content were reviewed, validated, and approved by the author.
·The author takes full responsibility for the accuracy, originality, and academic integrity of this submission.
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 10
AI DECLERATION

## Slide 11
ATU FINAL YEAR PROJECT
SEAN MALONEY
PAGE 11
DEMO VIDEO